## Slide 1
FSP – RA project
for iar keil
Date: 13/10/2022
Name: Khoa vo
Position, Department,
r-car middleware 2
Renesas Electronics Corporation

## Slide 2: Agenda
Preparation Page 03
Create new project Page 08
Migrating e2 Studio to keil Page 16
Ep automation Page 23

## Slide 3
preparation

## Slide 4: RA Smart Configurator
  The Renesas RA Smart Configurator (RA SC) is a desktop application designed to configure device hardware such as clock set up and pin assignment as well as initialization of FSP software components for a Renesas RA microcontroller project when using a 3rd-party IDE and toolchain.
  The RA Smart Configurator can currently be used with:
      Keil MDK and the Arm compiler toolchain
      IAR EWARM with IAR toolchain for Arm
  Download and Install (RASC) from https://github.com/renesas/fsp/releases

## Slide 5: Prerequisites
  RA Smart Configurator (RASC)
  KEIL:
    Keil MDK and Arm compiler
    Import the RA device pack. Download the RA device pack archive file (ex: MDK_Device_Packs_x.x.x.zip) from https://github.com/renesas/fsp/releases  Extract and run MDK_Device_Packs_vx.x.x.exe

## Slide 6: Link to Rasc
In Keil C select Tools  Customize Tools Menu
Select the new icon and fill in the fields
Arguments: -application com.renesas.cdt.ddsc.dpm.ui.dpmapplication configuration.xml "SL%L"
Arguments: Enter: --device $D –-compiler ARMv6 configuration.xml

## Slide 7: Link to Rasc
To reconfigure an existing project select
Tools > RA Smart Configurator
Manage Run-Time Environment  Flex Software  run Ra Configurator
To reconfigure the TrustZone partitions select
Tools > Device Partition Manager

## Slide 8
Create new project

## Slide 9: Create new project
  1. Open RA Smart Configurator (RASC)
  2. Chose Project Location and Project Name  Click Next

## Slide 10: Create new project
  3. Select FSP version,
  Board or Device
  and IDE Project type (Keil MDK)
   Click Next
  4. Select Project Type  Click Next

## Slide 11: Create new project
  5. Select RTOS (No RTOS, FreeRTOS or Azure RTOS)  Click Next
  6. Select Project Template  Click Finish and wait to Generating Project

## Slide 12: Create new project
  7. Config Project similar file configuration.xml in E2 Studio  Click Generate Project Content and wait to Generate Code

## Slide 13: Ra project in keil C
  Open Project in Folder (Location Project) file .uvprojx

## Slide 14: Ra project in keil C
  Right click Target 1  Option for Target 1:
  Tag Output
  Tag Debug

## Slide 15: Ra project in keil C
  Build / Rebuild
  Load project to specific board
  Start / Stop Debug

## Slide 16
Migrating e2 Studio to keil

## Slide 17: Migrating e2 Studio to keil
1. Create new project by copy template in Package Intaller ( ):
Choose Device/Board  Examples  Copy  Choose Location
Note: Don’t Start RASC (when keil launching)

## Slide 18: Migrating e2 Studio to keil
2. Rename project (Optional): Close Project  Rename file .uvprojx  Double click file .uvprojx to relaunch the project
  3. Copy file configuration (file .xml) and file pinconfig (file .pincfg) from folder project e2 Studio to folder project IAR

## Slide 19: Migrating e2 Studio to keil
4. Open RA Smart Configurator  Click Generate Project Content
If closing this section: Tools  RA Smart Configurator
In Keil click Yes to reload Project

## Slide 20: Migrating e2 Studio to keil
5. Copy folder src in project e2 Studio to project Keil
Open RA Smart Configurator  Click Generate Project Content again

## Slide 21: Migrating e2 Studio to keil
6. Build Project
7. Result

## Slide 22
Ep automation

## Slide 23: Build
Pre-requisite
Clone repo from: http://pbgitap01.sc.renesasam.com/systems_tataelxsi/ra_solutions.git
Checkout user’s respective branch, which contains the previous FSP version projects/EPs and pull the latest changes to local repo
Modify app_config.csv in ra_solutions/ep_automation before running the apps.
Property name | Purpose | Example of writing
Jlink_path | Windows PC J-Link installation path required for updating SEGGER_RTT sources files in src folder of EP | C:\Program Files (x86) \SEGGER\JLink_V686e
e2_path | Required for updating configuration.xml of e2studio EPs and calling CLI tool of e2studio for building. | C:\Renesas\RA\e2studio_v2020-10_fsp_v2.0.0
rasc_path | Required for updating configuration.xml of Keil and IAR supported EPs and their project content generation. | C:\Renesas\RA\sc_v2020-10_fsp_v2.0.0
keil_path | Required for calling CLI tools of Keil MDK for building Keil supported EPs. | C:\Keil_v5
iar_path | Required for calling CLI tools of IAR EW for building IAR supported EPs. | C:\Program Files (x86)\IAR Systems\Embedded Workbench 8.4
fsp_version | EP’s migration target FSP version | 2.0.0
build_logfileformat | Configurable naming convention for auto-generated build logs | ide_module_board_build_log.txt
associated parameters in app_config.csv

## Slide 24: Build
  Board specific EPs:
    Command> python runner_application.py -o build -i e2studio -b ek_ra2a1
    Building all the EPs of that board.
    Where -o is for selecting operation (build/rtt/review), -i for selecting IDE (e2studio, iar, keil) and -b for selecting board (ek_ra2a1, ek_ra4m1, etc.)
  EP specific boards:
    Command> python runner_application.py -o build -i e2studio -e gpt
    Building that EP on all supported boards.
    Where –e is for selecting EP (gpt, adc, ethernet, etc.)
Build Process

## Slide 25: Build
KEIL
python runner_application.py -o build -i keil -b ek_ra6m5
python runner_application.py -o build -i keil -e gpt
Result in Report file:
Result in Report file:

## Slide 26: Adding Project to folder example
Modify name and copy IAR and Keil C Project (migrating from e2 Studio) in Previous path to Example folder

## Slide 27: Adding Project to folder example
Run script automation build to check
Log file:
In report file:

## Slide 28
Renesas.com