## Slide 1: AUDIO SYSTEM
April, 2020

## Slide 2: AUDIO FRAMEWORK
    Overview
    Communication between CPU and ADSP
    Communication inside CPU
    Communication inside ADSP

## Slide 3: AUDIO FRAMEWORK
    1. Overview

## Slide 4: AUDIO FRAMEWORK
    1. Overview
The audio framework includes following modules:
Multimedia Framework: The framework is provided by OS to support audio playback. For WEA7, DirectShow is the target multimedia framework.
OMX IL Core: OMX interface to communicate between multimedia framework and OMX MC.
OMX MC: OMX IL media component of each codec.
ADSP Driver: Driver to control ADSP module.
Dispatcher: Communicate with ADSP Driver to get the command from CPU side (ARM) and send the response from ADSP side (ADSP).
uT-kernel: Real time OS is used for small embedded system.
SMAP: The framework which utilizes the services provided by uT-Kernel to control the codec execution.
Codec: Tensilica audio codec libraries

## Slide 5: AUDIO FRAMEWORK
    2. Communication between CPU and ADSP

## Slide 6: AUDIO FRAMEWORK
    3. Communication inside CPU - Send data to ADSP
    (1) - The multimedia framework submits the message
    (2) - The messages are added to the tail of command list of an OMX MC
    (3),(4) - If the command list is not empty, the Component thread reads the first element of command list (3) and sends it to Proxy (4)
    (5),(6) - Proxy writes this message to the shared memory (6) through the functions ADSP driver (5)
    (7),(8) - ADSP driver enables interrupt to ADSP side (7) to get data for encoding or decoding of ADSP side (8)

## Slide 7: AUDIO FRAMEWORK
    3. Communication inside CPU – Receive data from ADSP
(1), (2) When ADSP side finishes encoding or decoding a buffer, it writes message to shared memory (1) and enables interrupt to CPU side (2).
(3) When ADSP driver receives the interrupt from ADSP side, it wakes up all OMX IST of OMX MC
(4), (4’) When all OMX MC are waked up, they find the messages appreciated to themselves from shared memory through ADSP driver
(5) If they find comfortable messages, these messages are processed and added the tail of their response list
(6), (7), (8) If the response list is not empty, the Component thread reads the first element of response list (6) and sends it to multimedia framework through IL core (7), (8)

## Slide 8: AUDIO FRAMEWORK
    4. Communication inside ADSP
Initialize codec task: step (1) to (10)
Process the commands from CPU : step (1) to (11)
Destroy codec task: step (1) to (14)

## Slide 9: AUDIO FRAMEWORK
    4. Communication inside ADSP
(1), (2) CPU pushes a message to the command message queue (1) and raises an interrupt (2)
(3), (4) ISR task receives the interrupt and gets the message from command message queue (3), then sends it to factory task (4).
(5), (6) Factory task create codec task (5). After being created, codec task will push a response message to the internal message queue (6).
(7), (8), (9) ISR task gets the message from internal message queue (7), copies it to the response message queue (8) and raises an interrupt to CPU (9).
(10) CPU gets the message from response message queue
(11) ISR task send the message directly to the corresponding codec task
(12) The codec task sends the message to factory task
(13), (14) Factory task destroy the codec task (13) and push a response message to the internal message queue (14)

## Slide 10: ADSP SYSTEM
    Overview
    ADSP Driver
    ADSP framework
    ADSP Plugins
    Related HW module

## Slide 11: ADSP
    1. Overview

## Slide 12: ADSP SYSTEM
    2. ADSP Driver
    It includes 4 main parts:
  ADSP ALSA: It is an ALSA device driver, implements to register a sound card for ADSP device. It provides callback functions for the native supports from ALSA framework to perform both playback and record
  ADSP Driver Extension: It provides APIs for ADSP ALSA to connect to ADSP Driver (Proxy Extension Interface)
  ADSP Driver (Proxy Extension Interface): APIs of methods through which ADSP Driver Extension communicates with shared memory area in Hardware side
  CPU DAI: CPU DAI is the interface for the platform driver to communicate with other drivers

## Slide 13: ADSP SYSTEM
    2. ADSP Driver
    List of usage:
  Playback
  Capture
  TDM playback
  TDM capture
  Equalizer

## Slide 14: ADSP SYSTEM
    2. ADSP Driver – Playback
                Data path for playback
  SCU : Sampling Rate Converter Unit
  SRC : Sampling Rate Converter
  CTU : Channel Transfer Unit
  MIX : Mixer
  DVC : Digital Volume and Mute Function
  SSI : Serial Sound Interface

## Slide 15: ADSP SYSTEM
    2. ADSP Driver - Playback
Data path when mixing 3 streams
  SRC : Sampling Rate Converter
  CTU : Channel Transfer Unit
  MIX : Mixer
  SSI : Serial Sound Interface

## Slide 16: ADSP SYSTEM
    2. ADSP Driver – Capture
SRC : Sampling Rate Converter
DVC : Digital Volume and Mute Function
SSI : Serial Sound Interface
                Data path for capture

## Slide 17: ADSP SYSTEM
    2. ADSP Driver – TDM Playback
  SCU : Sampling Rate Converter Unit
SRC : Sampling Rate Converter
DVC : Digital Volume and Mute Function
SSI : Serial Sound Interface
                Data path for TDM playback

## Slide 18: ADSP SYSTEM
    2. ADSP Driver – TDM Capture
  SCU : Sampling Rate Converter Unit
SRC : Sampling Rate Converter
DVC : Digital Volume and Mute Function
SSI : Serial Sound Interface
                Data path for TDM playback

## Slide 19: ADSP SYSTEM
    3. ADSP Framework
ADSP Framework, ADSP Plugins,…

## Slide 20: ADSP SYSTEM
    4. ADSP Framework
                Architecture of ADSP Framework

## Slide 21: ADSP SYSTEM
    4. ADSP Plugins
Renderer/Capture Plugin
Equalizer plugin
TDM Renderer/Capture plugin
ADSP Framework
Codec
ADSP
ADSP Plugins
                ADSP in Hardware side
NC/EC

## Slide 22: ADSP SYSTEM
    5. Related HW module
SSI driver
SSIU driver
SCU driver
ADMAC driver
PDMA driver
FIFO driver

## Slide 23: Thank you