## Slide 1: Knowledge Sharing VISION IP - VIPDRV
Oct, 2022
Rev. 1.00 by Nguyen Huu Anh

## Slide 2: AGENDA
OVERVIEW
SW ARCHITECTURE
SW COMPONENTS
SW COMPONENT APIs
R-CAR 4th GENERATION
SW WORKFLOW

## Slide 3: 1. OVERVIEW
■ Image Processing Pipeline

## Slide 4: 2. SW ARCHITECTURE
2 types of SW components:
  Configuration Library - one per HW IP
  System Driver - one common across all IPs (until xOS2 this was separate per HW IP)
5 types of VisionIPs supported by HW: ACFv3x only, DOFall, STVv3x only, SMD-POSTv4h only, SMD-PSv4x only
SW components function:
  Configuration Library: prepares a configuration object (cfg, register values to be written to HW later)
  System Driver: push the cfg. values to HW & triggers HW processing (via DMA), monitor the processing done/error HW events (via interrupt)
■ Modules
■ SW components
■ Components Function
For details:VIPRSWP Software Architecture Specification

## Slide 5: 3. SW COMPONENTS
■ Application SW
User application to access all provided VIP functions
■ Config Library
Create config obj containing register values
Only interface to Application
■ System Driver
Enabling/disabling and (re-)configuration of the corresponding Vision-IP HW
Receive config obj from the Application
Provides access to hardware resources via OSAL layer
This layer maps the absolute address space window of the Vision-IP HW to a virtual address space accessible by the VIPDRV.
■ HW IP
■ OSAL
Embeds all necessary functions to interface to a System-On-Chip infrastructure, including DMA engine interrupts and safety errors controllers ...
Portability among each OSs by removing OS dependency from the application.
Notes: OSAL: Operating system abstract layer
Absolute address space
Virtual address space

## Slide 6: 4. SW COMPONENT APIs
- Init API - prepares a "default" configuration object
- Update APIs (specific to each IP) - update different parts of the configuration object
- Finalize API - checks range/validity of each parameter, calculates CRC for the register values
- Init API - initializes the SW resources required by the driver
- Start API - initializes the HW resources required by the driver
- Execute API - triggers DMA transfer (once register transfer is done this will trigger HW processing)
- Stop API - de-initialize the HW resources & stops ongoing processing
- Quit API - de-initialize the SW resources
■ Configuration Library
■ System Driver

## Slide 7: 5. R-Car 4th Generation
The Vision-IP (4th Generation) captures image data from the DDR-SDRAM and processes images.
Include DOF (optical flow vectors generation from a pair of images) and SMD-* cores (Structure from motion), and DMAC integrated each core acts as an accelerator for image processing at high speed. (Co-operation between hardware and software reduces the load on the CPU and improves the efficiency of image processing).
Exclude STV, ACF.
UMF or DOF: Dense type of Optical Flow vectors generation.
SMD-PS or SPS : Priority sampling.
SMD-POST or SPO : Post processing.

## Slide 8: 6. SW WORKFLOW
■ START / EXECUTE / STOP
Read two registers and check if equal to expected value
Spo_cb_ctl
.cb_status
.cbfunc
Validate cache of buffer using
R_OSAL_MmngrInvalidate
After HW raise any events, invoke the callback function
Flush input/output buffers
API: R_OSAL_MmngrFlush
Driver Steps | Flow State
Init | UNINIT -> INIT
Start | INIT -> READY
Execute | READY -> EXEC -> READY
Stop | READY -> INIT
Quit | INIT -> UNINIT
Lock mutex
Enable top-level INTC group
Set DMA registers and start DMA
Disable top-level INTC group
If use callback: Set User callback function
Unlock mutex
.cb_dma_status
.cb_sys_status
.cb_sys_err_status[]
…
Free buffers using
R_OSAL_MmngrDealloc

## Slide 9: 6. SW WORKFLOW
Config Library
App SW
System Driver
HW IP
OSAL
InitParam / changeParam / SetIn / SetOut
Step 1. App request cfg. Object init & update

## Slide 10: 6. SW WORKFLOW
Config Library
App SW
System Driver
HW IP
OSAL
InitParam / changeParam / SetIn / SetOut
Step 1. App request cfg. Object init & update
Step 2. ConfLib fills in cfg (reg) value & DMA

## Slide 11: 6. SW WORKFLOW
Config Library
App SW
Push cfg to HW
Trigger the HW processing
HW IP
OSAL
InitParam / changeParam / SetIn / SetOut
Finalize
Step 1. App request cfg. Object init & update
Step 2. ConfLib fills in cfg (reg) value & DMA
Step 3. Cfg final / overall consistency check

## Slide 12: 6. SW WORKFLOW
Config Library
App SW
Push cfg to HW
Trigger the HW processing
HW IP
OSAL
InitParam / changeParam / SetIn / SetOut
Finalize
Step 1. App request cfg. Object init & update
Step 2. ConfLib fills in cfg (reg) value & DMA
Step 3. Cfg final / overall consistency check
Step 4. push cfg to HW & trigger execution / processing

## Slide 13: 6. SW WORKFLOW
Config Library
App SW
Push cfg to HW
Trigger the HW processing
HW IP
OSAL
InitParam / changeParam / SetIn / SetOut
Finalize
Int : end processing
Step 1. App request cfg. Object init & update
Step 2. ConfLib fills in cfg (reg) value & DMA
Step 3. Cfg final / overall consistency check
Step 4. push cfg to HW & trigger execution / processing
Step 5. HW processing done

## Slide 14: 6. SW WORKFLOW
Config Library
App SW
Push cfg to HW
Trigger the HW processing
HW IP
OSAL
InitParam / changeParam / SetIn / SetOut
Finalize
Int : end processing
Poll DRV status
Step 1. App request cfg. Object init & update
Step 2. ConfLib fills in cfg (reg) value & DMA
Step 3. Cfg final / overall consistency check
Step 4. push cfg to HW & trigger execution / processing
Step 5. HW processing done
Step 6. App get status (w/o CB)

## Slide 15: 6. SW WORKFLOW
Config Library
App SW
Push cfg to HW
Trigger the HW processing
HW IP
OSAL
InitParam / changeParam / SetIn / SetOut
Finalize
Int : end processing
Call app CB
Step 1. App request cfg. Object init & update
Step 2. ConfLib fills in cfg (reg) value & DMA
Step 3. Cfg final / overall consistency check
Step 4. push cfg to HW & trigger execution / processing
Step 5. HW processing done
Step 6. App get status (w/ CB)

## Slide 16
App SW
p_IN_img
cfg_val
cfg reg val
DMA cfg
p_OUT_buf
img
out buff
Step1: App requests cfg. object init & update
1
initParam / changeParam / setIn / seOut
ID

## Slide 17
App SW
p_IN_img
cfg_val
cfg reg val
DMA cfg
p_OUT_buf
img
out buff
Step2: ConfLiB fills in cfg (reg) values & DMA
1
2
ID
initParam / changeParam / setIn / seOut

## Slide 18
App SW
p_IN_img
cfg_val
cfg reg val
DMA cfg
p_OUT_buf
img
out buff
Step2a: cgf Obj final / overall consistency check
1
2
ID
2a
finalize

## Slide 19
Update
cfg obj
App SW
1) push cfg to HW
2) trigger the HW processing
HW IP
p_IN_img
cfg_val
cfg reg val
DMA cfg
p_OUT_buf
img
out buff
Step3: push cfg to HW & trigger execution/processing
1
2
3
3
finalize
ID
flag

## Slide 20
Update
cfg obj
App SW
1) push cfg to HW
2) trigger the HW processing
HW IP
p_IN_img
cfg_val
cfg reg val
DMA cfg
p_OUT_buf
img
out buff
Step 4: HW processing done
1
2
3
3
4
int: end processing

## Slide 21
Update
cfg obj
App SW
1) push cfg to HW
2) trigger the HW processing
HW IP
p_IN_img
cfg_val
cfg reg val
DMA cfg
p_OUT_buf
img
out buff
Step 5: App gets status (w/o CB)
1
2
3
3
4
int: end processing
poll DRV status
5

## Slide 22
Update
cfg obj
App SW
1) push cfg to HW
2) trigger the HW processing
HW IP
p_IN_img
cfg_val
cfg reg val
DMA cfg
p_OUT_buf
img
out buff
Step 5: App gets status (w/ CB)
1
2
3
3
4
int: end processing
call app CB
5

## Slide 23
Update
cfg obj
App SW
1) push cfg to HW
2) trigger the HW processing
HW IP
p_IN_img
cfg_val
cfg reg val
DMA cfg
p_OUT_buf
img
out buff
Step3: ConfLiB fills in cfg (reg) values & DMA
1
2
3

## Slide 24
App SW
request to “fill” confObj:
changeParam - setInput - finalize
confObj filled
write cfg.
trigger processing
1
2

## Slide 25
Cam
Application
CPU
fusion
2
filter
(ISP / IMR)
Image processing
(DOF / STV / ACF)
Image processing
(DOF / STV / ACF)
Image processing
(DOF / STV / ACF)
VIP SW

## Slide 26: Thank you